## Slide 1: Trima Install Scripts
Installs new version of Trima SW on the machine
Checks versions to make sure it is compatible with the hardware
Converts config files between versions
  Uses “base versions” (5.10 & 6.00) as intermediate conversion steps

## Slide 2: Source Files
Code is in ../Trima/Install/InstallCommon
  updateTrima.h/cpp
  updateTrimaBase.h/cpp
  updateTrima5X.h/cpp
  updateTrima6X.h/cpp
  updateTrima###.h/cpp (### is version number)
    One for every functionally equivalent version
  /Install5X and /Install6X are the build areas for VxWorks 2.02 and 2.2 versions of the scripts

## Slide 3: updateTrima.h/cpp
Figures out what is installed, what is to be installed, what the hardware is, if install is allowed
Determines SW versions based on build numbers
Extracts source files
updateTrima() is the entry point from VxWorks
Calls update() for appropriate new version
.cpp is modified for new versions of Trima SW

## Slide 4: updateTrimaBase.h/cpp
Contains the code that installs new config files and modifies config.dat as needed
updateConfig…() functions convert config.dat from one version to closely related ones
  Called by updateConfigVersion() in updateTrima### classes
  Used in series for longer conversions
.h contains the version number enum
  Gets updated for new versions of Trima SW

## Slide 5: updateTrima5X & update Trima6X
Abstract classes for common 5.X (VxWorks 2.02) and 6.X (VxWorks 2.2) functionality

## Slide 6: updateTrima###.h/cpp
Contains version specific functions overridden from updateTrima5X/6X
updateConfigVersion() specifies what updateConfig…() functions in updateTrimaBase to call to correctly convert the config.dat files
Have to update updateConfigVersion() for each new Trima version

## Slide 7: Adding New Trima Version
Information to gather before starting:
  What existing version the new one is derived from (its parent version).
  If the new Trima SW version changes the config.dat from its parent version OR has any other version-specific changes.
    If it doesn’t, it is “functionally equivalent” to its parent.
  How to distinguish it from other versions using the build number.

## Slide 8: Adding New Trima Version con’t
If it is functionally equivalent to its parent version, go to step 2, otherwise:
  Create a new updateTrima###.h/cpp for that version using the nearest existing version as a model
  Add a updateConfigxxx() function to updateTrimaBase to convert the config.dat from the nearest version

## Slide 9: Adding New Trima Version con’t
  Add the new cpp file to the update_cxx_files define in the Install5X and Install6X makefiles

## Slide 10: Adding New Trima Version con’t
updateTrimaBase.h:
  Add the new version to TrimaVersion enum in updateTrimaBase.h
  Add it before the NUMBER_OF_VERSIONS value
UpdateTrima.cpp
  Add a true/false to the allowedPythonUpgrade[] array to indicate if that version can be installed on a Trima with a Python control computer

## Slide 11: Adding New Trima Version con’t
UpdateTrima.cpp
  In init():
    Add a block to create an object of the new version (if needed) and a versionMap entry
    Add an entry in the versionStringMap for that version – found under the comment:
    // Initialize the printable version strings
  In parseRevision() modify the switch stmt to set the parsedVersion based on the new version’s build information

## Slide 12: Adding New Trima Version con’t
In all of the updateTrima###.cpp files
  Add the new version to the switch statement to convert the config.dat correctly
    This is the “from” version, so in the updateTrima610.cpp the “case V600:” is how to convert the 6.00 config.dat to the 6.10 format
Compile and test.